Operation Manual

MENU key: Main Manu / Return

OK   key: Enter key / Division, Cycle, Fixed Frequency

↔    key: left and right option key

↕ / REC: Up and Down option key / Record key

TF Card (certified products): Need to format first, select FAT32 format.

(Notes: Each pair of camera has been matched frequency before they dispatched from the factory. Users only need to connect them to power, and then it can collect the images. If the screen can’t show normal images by pressing the wrong key, only have to cut off the electricity of receiver and reconnect it, and it will restore to initial position.)

- First press the "MENU" ,then enter main menu, "CAMERA SETUP" (match frequency), "PLAY LIST "(file of video), "SYSTEM SETUP" (time setup and format switching) will be displayed on the screen.

- Use "↔ " to select CAMERA SETUP, press "OK" to confirm camera setup, at this time, "1,2,3,4 "will display on the screen,then connect camera with power, and first choose 1 , press "OK ", then press the "SET"of the camera, after connection, "CAMERA SETUP, PAIR OK "will show up on the screen, the first camera success in setting up. Press "MENU" again, go back to main menu, use "↔ " to select 2, connect the second camera with power, press "OK",then press "SET"of second Camera, match frequency for second camera. Use the same method to set up the third and forth camera, press" MENU" go back to main menu.

- Back to main menu, use" ↔ " enter "SYSTEM SETUP" to set up time and system. When setting up them, use" ↔ "and "↕" to select time and system what you want, it will be successful after press OK to confirm. After finished, press"MENU " back to main menu.

- Back to main menu, the images of about four different cameras will display on the screen simultaneously at the same time. If you press "OK ", the four pictures will display round. When it display the image what you want, press "OK" key again, it will fix to the exact image as you required.

- Insert TF card ,press "↕" key, (all the four video) will be displayed on the screen, and system will record the images gathering by each camera. Press"↕"again, system stop recording.

- If you want to check the recorded video, you should stop recording first, and enter into main menu, down to PLAY LIST, select the recording date and exact time of the video to playback. You can also insert TF card to PC and use self-support software and player software to play.